## Slide 1
Mirror for Bell's Palsy
A local-first facial retraining companion that turns invisible recovery into measurable practice.
mirror.iali.in
Ali Mustufa

## Slide 2
WHY THIS MATTERS
The executive thesis
02
Mirror for Bell's Palsy · mirror.iali.in
Bell's palsy recovery depends on feedback, but the patient cannot reliably feel or see the millimetres that matter. Mirror converts webcam geometry into practice-grade signals, while keeping the product local, private, and conservative.
Invisible
recovery
Custom
measurement layer
Actionable
practice loop
Problem
Algorithm
Product

## Slide 3
PROBLEM
The patient problem is a broken feedback loop
03
Mirror for Bell's Palsy · mirror.iali.in
“
When half your face won't move, the mirror stops being useful.
Can't feel
Can't see
Can't trust
Skip reps
WHAT RECOVERY ASKS FOR
Daily, gentle, repetitive movement
Evidence that effort is changing something
Confidence that a bad capture is not “bad recovery”
Without measurement, motivation becomes guesswork.

## Slide 4
PRODUCT
Mirror at a glance
04
Mirror for Bell's Palsy · mirror.iali.in
A practice companion, not a clinician. It guides exercises, tracks webcam landmarks with MediaPipe, scores balance and affected-side movement, and helps users export useful evidence.
Guided practice
Forehead, eyes, nose, cheeks, mouth, vowels, and expression-style movements.
Real-time scoring
Live left/right symmetry plus affected-side movement against personal baselines.
Progress memory
Sessions, journals, streaks, trend charts, report images, and assessments saved locally.
Review output
Printable reports, clinician bundles, and validation exports when the user chooses.
Primary URL: mirror.iali.in · Demo: mirror.iali.in/try

## Slide 5
USER JOURNEYS
Two product surfaces, one measurement core
05
Mirror for Bell's Palsy · mirror.iali.in
The demo gets trust in seconds; the practice app builds longitudinal recovery evidence. Same tracker, different decision context.
/TRY DEMO
Instant tracker proof
478-point mesh color-coded by region
Ranked muscle activations with left/right bars
Live expression chip and head-position readout
No session machinery or scoring lock
FULL PRACTICE APP
Measured recovery loop
Camera setup → calibration → exercise hold → feedback
Movement profile, adaptive plan, comfort dosing
Assessment trend, journal, reports, local exports
Unscored guided practice still works when camera/model fails
shared measurement core

## Slide 6
SYSTEM VIEW
Architecture: local-first by construction
06
Mirror for Bell's Palsy · mirror.iali.in
The pipeline is intentionally boring in the right places: browser camera, on-device inference, custom scoring, IndexedDB, explicit export. No account. No practice-data backend.
Camera
frame
browser permission
MediaPipe
Face Landmarker
478 mesh + blendshapes + pose
Mirror
scoring layer
calibration, gates, exercises
IndexedDB
local memory
sessions, images, profiles
User-chosen
report/export
PDF, JSONL, backup
Worker-backed detector where supported, main-thread fallback where not.

## Slide 7
MODEL BOUNDARY
The model does geometry; Mirror does judgment
07
Mirror for Bell's Palsy · mirror.iali.in
This distinction matters. MediaPipe is the sensor; Mirror is the scoring product. Mixing those up would make the deck sound like demo-day fog machine nonsense.
MEDIAPIPE PROVIDES
478
3D landmarks
blendshapes
blink, brow, smile, sneer
pose
facial transform matrix
Loaded on-device with GPU delegate; inference uses Face Landmarker 0.10.21 runtime.
MIRROR ADDS
Neutral calibration and noise floors
Pose-normalized face-local scoring
Exercise-specific directional logic
Affected-side progress against baselines
Reports, diagnostics, safety copy

## Slide 8
CALIBRATION
Capture trust stack: score only when the data deserves it
08
Mirror for Bell's Palsy · mirror.iali.in
Mirror is conservative by design. If evidence is weak, the better answer is silence or coaching—not a confident-looking number wearing a cheap suit.
01
Setup quality
face presence · lighting · distance · FPS · stability · glare risk
02
Neutral calibration
24 stable frames · per-landmark jitter · neutral pose matrix
03
Hold-frame gates
head-pose deviation < 0.20 rad · movement above noise
04
Scoring diagnostics
drop reasons · rejected frames · capture flags · safety notes
Calibration: CALIBRATION_FRAMES = 24, stability epsilon = 0.006, center offset < 0.12, eye-line tilt < 0.12 rad.

## Slide 9
ALGORITHM
Updated normalization: measure the face, not the camera wobble
09
Mirror for Bell's Palsy · mirror.iali.in
The scorer now prefers MediaPipe's 3D facial transformation matrix, converting landmarks into a face-local coordinate frame before comparing movement.
BEFORE
Screen-space landmarks
Head tilt, distance, and yaw can masquerade as movement.
AFTER
Face-local frame
Translate to nose tip
Apply inverse pose rotation
Scale by 3D inter-ocular distance
Residual eye-line roll correction
Practical result: translation, roll, scale, and much yaw/pitch foreshortening get reduced before scoring.

## Slide 10
ALGORITHM
Scoring engine: route each movement to the right scorer
10
Mirror for Bell's Palsy · mirror.iali.in
Generic distance scoring is lazy. A brow raise, nostril flare, smile, and pucker do not move the same way. Mirror routes exercises to purpose-built scorers.
Exercise
ID
Scorer
router
Pairwise
displacement
Directional
movement vectors
Specialized
brow / nose
OUTPUT CONTRACT
leftDisp
rightDisp
symmetry
peak
all in user/anatomical left-right

## Slide 11
ALGORITHM DETAILS
Movement families now have movement-specific logic
11
Mirror for Bell's Palsy · mirror.iali.in
The updated algorithm counts the intended direction, not merely “any landmark moved.” That is how you stop wrong movement from being rewarded.
Family
Signal counted
Why it matters
Smile · vowel E/I
outward + slightly upward mouth pull
prevents pucker from scoring as smile
Pucker · kiss · vowel O/U
inward lip motion toward midline
prevents smile-only movement from scoring
Eye close · blink · wink
decreased eyelid aperture
rejects lateral eye drift
Brow raise / frown
brow-eye gap; frown down/inward
stable against absolute brow position
Nostril flare / scrunch
rim/ala aperture; upward lift + sneer blendshape
no fallback to generic if direction fails
Blendshapes help activation and snapshot timing. They are not the main symmetry score because coefficients can look artificially balanced on asymmetric faces.

## Slide 12
MEASUREMENT MODEL
The metric split: balance is not recovery
12
Mirror for Bell's Palsy · mirror.iali.in
A symmetry score can stay flat while the affected side genuinely gets stronger. The updated deck makes that distinction explicit.
MOVEMENT BALANCE
symmetry = min(left, right) / max(left, right)
Best for: “was this rep balanced?”
Not enough for: “am I recovering?”
RECOVERY PROGRESS
affectedProgress = current affected / first baseline affected
Also tracks affected-to-proper ratio today versus baseline.
Example: “Right smile is +18% from first baseline. Affected-vs-proper is 62% today, up from 48%.”

## Slide 13
PERSONALIZATION
Personal movement profile: baseline as a living layer
13
Mirror for Bell's Palsy · mirror.iali.in
The profile is not a trained model. It is a local, individualized baseline and threshold system generated from the user's own movement.
Affected side
+ comfort
left / right / both / unsure · gentle / normal / advanced
Global neutral
calibration
stable frames · noise floor · neutral matrix
Per-exercise
rest neutral
less drift from blinking, jaw settling, tension
Robust baseline
top 20% movement window, not single peak
Quality label
Strong · Usable · Retake
Threshold bands: minimumVisible = 20% of peak floor 0.002 · reliableMovement = 35% of peak floor 0.004 · baselineTarget = max peak
Nose baselines use lower nose-specific thresholds because nostril flare is typically only 1–2% of inter-ocular distance.

## Slide 14
PRODUCT INTELLIGENCE
Adaptive practice: recommendations with guardrails
14
Mirror for Bell's Palsy · mirror.iali.in
The app prioritizes useful practice without pretending noisy scores are insight. This is the part where “move fast” would have shipped dangerous nonsense.
INPUTS
Baseline symmetry
Affected-side progress
Affected/proper ratio
Recent session quality
Journal fatigue / pain prompts
Quiet-region coactivation risk
Adaptive
plan ranking
no intensity boost from stale / noisy / risky evidence
OUTPUTS
Daily focus movements
Comfort-level dose
Live baseline-relative feedback
Trend status: collecting, stable, improving, low confidence

## Slide 15
ASSESSMENT
Standard assessments make progress reviewable
15
Mirror for Bell's Palsy · mirror.iali.in
Daily practice and standardized assessment should not be mashed together. Mirror stores assessment records separately so trends can be compared cleanly.
FIXED MOVEMENT SET
01
Eyebrow raise
02
Gentle eye closure
03
Open smile
04
Nose wrinkle / snarl
05
Lip pucker
STORED RECORD
Rest metrics
palpebral fissure · midface proxy · mouth-corner height
Voluntary movement
brow / eye / midface-nose / mouth zones
Coactivation risk
quiet-region movement during intended movements
Report linkage
source session images and printable report
Assessment sessions do not count toward daily practice goals or streaks.

## Slide 16
NON-NEGOTIABLE CAVEAT
Clinical-scale estimates: useful, fenced, not clinical grades
16
Mirror for Bell's Palsy · mirror.iali.in
Dedicated caveat, because this is where sloppy decks get people in trouble. Mirror can show scale-inspired self-tracking estimates, but it does not diagnose, grade paralysis, or replace clinician assessment.
DISPLAY EVIDENCE GATE
60%
usable standard-assessment movement coverage
plus complete resting asymmetry metrics and usable/strong capture quality where present.
ESTIMATES PRODUCED
House-Brackmann-inspired global estimate
Sunnybrook-style composite estimate
eFACE-style static / dynamic / synkinesis proxies
v5: partial estimates omit weak/missing movements instead of treating them as zero.
VALIDATION RELEASE GATE
80%
observed agreement + Wilson lower bound
Requires reviewed clinical labels, 30 assessments, 10 distinct cases, source hashes, reviewer controls, and status update.
Current status: clinicalFacingScoresAllowed = false. The app remains estimate-only until reviewed evidence exists.

## Slide 17
OUTPUTS
Reports and exports turn practice into reviewable evidence
17
Mirror for Bell's Palsy · mirror.iali.in
The user controls every export. Mirror packages context, quality, and trend evidence so a clinician is not staring at a naked score with no provenance.
EXPORT 1
Printable report
Session date, comfort level, setup quality, symmetry, per-rep chips, affected-side progress, baseline/current images, safety notes.
EXPORT 2
Clinician bundle
JSONL review package with assessments, comparisons, sessions, journal notes, quality flags, selected images, frame samples.
EXPORT 3
Validation dataset
Opt-in JSONL with frame samples, assessment scale rows, label templates, source context, and replay metadata.
Backup import/export is separate from clinician/validation JSONL. That separation is boring and exactly why the data model is not a junk drawer.

## Slide 18
PRIVACY
Privacy posture: local-first, explicit-share only
18
Mirror for Bell's Palsy · mirror.iali.in
A face-tracking product only earns trust if the privacy model is not a footnote. Mirror's practice data stays in the browser unless the user exports it.
STAYS LOCAL
Camera frames processed in browser by MediaPipe
No uploaded video or Mirror practice-data backend
Sessions, landmarks, profiles, journal, images in IndexedDB
Optional local recovery model trains from saved device data
LEAVES ONLY BY USER CHOICE
Print/save report as PDF
Export clinician bundle JSONL
Export validation dataset JSONL
Clear site data to remove local Mirror data
Hosting caveat: Render may process normal hosting metadata. Mirror's code does not use it for practice-data collection or profiling.

## Slide 19
READINESS
Validation framework: tooling ready, clinical evidence pending
19
Mirror for Bell's Palsy · mirror.iali.in
The repo now has a release-gated validation workflow. The honest status is stronger than hand-waving: tooling exists; reviewed clinical datasets do not.
CURRENT STATUS
tooling-ready
needs-reviewed-data
Reviewed datasets
Production threshold calibration
IMPLEMENTED WORKFLOW
Validation JSONL export
Blinded clinical review package
Label merge + reviewer agreement
Replay evaluation + threshold calibration
Clinical-readiness + release status checks
FUTURE RELEASE GATES
30 reviewed assessments
10 distinct validation cases
80% observed + Wilson lower bound
HB case-mix floors
Source SHA-256 traceability

## Slide 20
BUILD
Technology stack: modern, local, lightweight
20
Mirror for Bell's Palsy · mirror.iali.in
The stack is intentionally client-heavy: fast to ship, easy to host, and aligned with the privacy promise.
React 19
UI + practice flow
Vite 8
build runtime
Tailwind 4
interface system
MediaPipe
vision model
IndexedDB
local persistence
Also: Recharts for progress charts · Lucide icons · WebAssembly / WebGL · worker-backed detector with fallback · OpenAI Codex, Claude Opus, and Pieces in the build workflow

## Slide 21
WHAT NEXT
Roadmap: where the next credibility comes from
21
Mirror for Bell's Palsy · mirror.iali.in
Most core algorithm upgrades are implemented. The next value is not more sparkle; it is validation, threshold calibration, and cleaner review workflows.
TRACK 1
Now implemented
Worker-backed inference
Directional scorers
Setup quality + diagnostics
Assessment mode + exports
Validation label workflow
TRACK 2
Pending evidence
Clinician-reviewed datasets
Production threshold calibration from reviewed reports
Clinical-scale agreement proof
Reviewer-agreement proof
TRACK 3
Product polish
Portable progress import/export
Clearer calibration coaching
Better clinician handoff summaries
More replayable audit trails
Design principle: do not make the app look clinically “official” until the evidence is actually official. Restraint is the feature.

## Slide 22
TRACTION
Distribution: the story already has pull
22
Mirror for Bell's Palsy · mirror.iali.in
The origin story landed because it is specific: one person, a sudden diagnosis, and a working tool built out of real need.
9+
publications picked up the story
May 2026
media attention window
local-first
privacy narrative, not just tech demo
Featured across Hindustan Times, Times of India, Mint, Free Press Journal, NewsBytes, What's Hot, MSN, LiveMint, Dailyhunt and others.
Executive framing: press proves resonance, not clinical validity. Keep those lanes clean.

## Slide 23
CTA
Try it yourself
23
Mirror for Bell's Palsy · mirror.iali.in
The executive story is simple: see the tracker immediately, then understand the full practice loop.
SEE THE TRACKER
mirror.iali.in/try
Standalone face mesh, activation bars, expression detector, head-position readout.
FULL PRACTICE APP
mirror.iali.in
Guided practice, calibration, baseline profile, trends, reports, and exports.
Medical caveat travels with the product: practice and self-tracking only; work with a qualified clinician.

## Slide 24
CLOSING
From invisible recovery
to measurable practice.
Mirror does not promise recovery. It gives people a private, repeatable way to see whether their practice is changing over time.
BUILT BY
Ali Mustufa
X / Twitter · @ialimustufa · LinkedIn · in/ialimustufa
SUPPORTED BY
OpenAI · Render · MediaPipe · Claude · Pieces
Sources: repository README and docs, original talk deck, privacy policy, model/scoring notes, clinical-scale estimate notes.
mirror.iali.in